## Slide 1
EE 151
APPLIED ELECTRICITY
2018.09.03
Ing. Dr. Abdul-Rahman Ahmed

## Slide 2: EE 151: APPLIED ELECTRICITY
Course Structure: 3 2 3
Course Instructor: Ing. Dr. Abdul-Rahman Ahmed
aarahman.soe@knust.edu.gh
0508 – 351 - 438
Course Materials: https://www.rfmicrowaveknust.com
Teaching Assistants: Akambole Isaac Ageebase Alberta Oduraa Quartey
0506257842 0547886101
akamboleisaac@gmail.com oduraa2000@gmail.com

## Slide 3: Website QR Code

## Slide 4: Course Objective
Appreciate basic principles of Electrical Circuits
Be equipped with tools required to analyze
  electric and
  magnetic circuits
Develop knowledge and fundamental concepts associated with Electrical/Electronics Engineering

## Slide 5: Course Outline
Unit 1: Circuits and Network Theorems:
  Kirchhoff's laws, Thevenin’s Theorem, Norton's Theorem, Superposition Theorem, Reciprocity Theorem and Delta- Star Transformation.
Unit 2: Alternating current circuits
  Determination of Average and RMS values, Harmonics, Phasors, impedance,current and power in ac circuits
Unit 3: Three-phase circuits
  Connection of three-phase windings, three phase loads, power in three-phase circuits, solving three-phase circuit problems
Unit 4: Magnetic circuits – Components and terminologies, solving magnetic circuit problems

## Slide 6: Course Calendar
Week | Week Beginning | Topic
1 | 3rd September | Network Theorems
2 | 10th September | Network Theorems
3 | 17th September | AC Circuits
4 | 24th September | AC Circuits
5 | 1st October | 3-Phase Circuits
6 | 8th October | 3-Phase Circuits
7 | 15th October | Magnetic Circuits
8 | 22nd October | Revision/Tutorial
9 | 29th October | Revision/Tutorial
10 | 5th November | Mid-Semester Exams
11 | 19th November | Magnetic Circuits
12 | 26th November | Revision/Tutorial
13 | 3rd December | End of Semester Exams (to be confirmed)

## Slide 7: Recommended Texts

## Slide 8: Course Delivery Method
Lectures
Tutorials
Circuit Design
Simulations
Laboratory work

## Slide 9: Classroom Manners
No phone usage
No eating
No noise-making
No lateness
No gossiping
No sleeping
Etc…

## Slide 10: ASSESSMENT
Quizzes
Mid-semester examination
End of semester examination 70%
Total 100%
30%

## Slide 11: UNIT 1: CIRCUIT AND NETWORK THEOREMS
Definition of a circuit
  An interconnection of elements forming a closed path along which current can flow.
Elements of an electric circuit
  Active elements: Energy producing elements eg. Batteries, Generators, solar cells etc.
  Passive elements: Energy using elements eg. Resistors, inductors, capacitors

## Slide 12: Circuit Terminologies
Node (Junction)
  A point where currents split or come together [ points c, d, e and f]
Path
  Any connection where current flows [eg bc, be, etc]

## Slide 13: Circuit Terminologies
Branch
  A connection (path) between two nodes [eg. cd, cb, ad, df]
Loop/Mesh
  a closed path of a circuit [ eg. cghdc]

## Slide 14: Circuit Terminologies
Short-circuit
  A branch of theoretically zero resistance.
  It diverts to itself all currents that would have flown in adjacent branches (branches hooked to the same node); except branches with sources.

## Slide 15: Circuit Terminologies
Short-circuit cont.
Self assessment
  Which of the resistors in the circuit below have been short-circuited?
Ans: R2 and R3

## Slide 16: Circuit Terminologies
Open circuit – A branch of theoretically infinite resistance. It prevents current from flowing in its branch

## Slide 17: Resistors in Series
Resistors are in series
  when the same current flows through them.
  There is NO JUNCTION between them.
  In Fig. 1 : R1 and R2 are in series
  In Fig. 2: None of the resistors are in series

## Slide 18: Resistors In Series
Self assessment 1
  Which of the following resistors are in series?
ANS: R1&R2, R3 & R4 and R5 & R6

## Slide 19: Resistors in Series
Total (effective) resistance of series resistors
  total resistance RT for resistors R1, R2, R3, ….., RN which are in series if given by:

## Slide 20: Resistors in Parallel
Resistors are said to be in parallel when the voltage across them is the same.

## Slide 21: Resistors in Parallel
Colloquially, TWO resistors are in parallel if it is possible to move from one to the other without passing through another element. i.e., the two can be circled without passing through another circuit element.

## Slide 22: Resistors in Parallel
Self assessment
Which of the resistors in the circuit below are in parallel?

## Slide 23: Resistors in Parallel
Total resistance
When resistors R1 and R2 are in parallel, the total resistance RT is given by:

## Slide 24: Effective Resistance of a Circuit
Effective circuit resistance is found by
  identifying and putting together series and or parallel resistors
  Eg 1. Find the total resistance of the circuit below.

## Slide 25: Effective Resistance of a Circuit
Find the effective resistance of the circuit

## Slide 26: Effective Resistance of a Circuit
Self Assessment 1
  Find the total resistance of the circuit below.

## Slide 27: Effective Resistance of a Circuit
Self Assessment 2
  Find the total resistance of the circuit below.

## Slide 28: Current Division Rule
The current division rule is applied to share current between parallel branches. Consider the circuits below

## Slide 29: Current Division Rule
Similarly,

## Slide 30: Current Division Rule
In summary

## Slide 31: Current Division Rule
Consider the circuit below

## Slide 32: Current Division Rule
Example 1
  Find the values of I1 and I2 in the circuit below.

## Slide 33: Current Division Rule
Example 2
  Find the value of I1 in the circuit below.

## Slide 34: Voltage Drop
Any time a voltage drives current through a resistor, some of the voltage drops across the resistor.
The magnitude of the drop is the product of the resistance and current

## Slide 35: Voltage Drop
Example
  Find the values of I and R in the circuit below.
Solution
Voltage across 3Ω resistor = 10 – 4 = 6V
Current in 3Ω resistor = I = 6/3 = 2A
Resistance R = 4V/I = 4/2 = 2Ω

## Slide 36: Revision Exercise
Find the value of I in the circuit below.

## Slide 37: Revision Exercise
Thus

## Slide 38: Revision Exercise

## Slide 39: Group Assignment 1
  Find the value of the current in all resistors of the circuit below using total resistance and voltage drop principles. DO NOT use current division rule.

## Slide 40: Kirchhoff's Current Law(KCL)
The Law
The sum of currents entering a node equals the sum of currents leaving the node.
Sum of currents entering
Sum of currents Leaving

## Slide 41: Kirchhoff's Current Law(KCL)
Example
Find the value of i in the figure below.
Solution

## Slide 42: Kirchhoff's Current Law(KCL)
Self assessment
Find the value of i in the figure below.
ANS

## Slide 43: Kirchhoff's Voltage Law(KVL)
The law
The algebraic sum of the voltages in a loop (closed path) equals zero. Alternatively, in a loop, the algebraic sum of voltage sources equals the algebraic sum of voltage drops.
Loop abgha
Loop adeha

## Slide 44: Kirchhoff's Voltage Law(KVL)
Loop cbgfc
Loop acfha

## Slide 45: Kirchhoff's Voltage Law(KVL)
Example 1
Find the current in all parts of the circuit below.
Applying KVL to loop bcdab
Applying KVL to loop ecdfe

## Slide 46: Kirchhoff's Voltage Law(KVL)
Applying KCL to node c:
Solving the equations simultaneously yields

## Slide 47: Kirchhoff's Voltage Law(KVL)
Example 2
Find the currents in all parts of the circuit below.
Solution
Apply KVL to loop cefdc

## Slide 48: Kirchhoff's Voltage Law(KVL)
Apply KVL to loop abcda:
Apply KVL to loop ghfeg:

## Slide 49: Kirchhoff's Voltage Law(KVL)
Solving the three equations:
Simultaneously,

## Slide 50: Thevenin’s Theorem
Theorem:
Any linear circuit connected between two terminal can be replaced by a Thevenin’s voltage(VTH) in series with a Thevenin's resistance (RTH).
VTH is the open-circuit voltage across the two terminals
RTH is the resistance seen from the two terminals when all sources have been deactivated

## Slide 51: Thevenin’s Theorem
To find the current through a resistor in a circuit, the following steps are taken:
Remove the resistor from the circuit and mark the two terminals.

## Slide 52: Thevenin’s Theorem
2. Find the open-circuit voltage (VTH) across the two terminals by applying KVL. Treat VTH as a source

## Slide 53: Thevenin’s Theorem
3. Recall the circuit created before step 2 and deactivate all sources. Short-circuit voltage sources and Open-circuit current sources.

## Slide 54: Thevenin’s Theorem
4. Find the total resistance of the circuit resulting from step 3 as
seen from the two terminals

## Slide 55: Thevenin’s Theorem
Reproduce the Thevenin’s equivalent circuit and connect the resistor whose current is to be found.

## Slide 56: Thevenin’s Theorem
6. Calculate the current in the circuit in step 5. This is the current being sought for.

## Slide 57: Thevenin’s Theorem
Example 1
Using Thevenin’s theorem, determine the current in the 3-Ω resistor of the circuit below.
Solution
Steps 1 & 2

## Slide 58: Thevenin’s Theorem
Applying KVL to loop dcbed:
Applying KVL to loop fabef:

## Slide 59: Thevenin’s Theorem
Substituting for I in equation 1
Steps 3 & 4

## Slide 60: Thevenin’s Theorem
Steps 5 & 6

## Slide 61: Thevenin’s Theorem
Example 2
Find the current in the 10-Ω resistor of the circuit below using Thevenin’s theorem.
Solution
Steps 1 & 2

## Slide 62: Thevenin’s Theorem
Applying KVL to loop cbgfc:
Applying KVL to loop abgha:
Applying KVL to loop dcfed:

## Slide 63: Thevenin’s Theorem
Substituting for I1 and I2 in equation 1 yields:
Steps 3 & 4

## Slide 64: Thevenin’s Theorem
Steps 5 & 6

## Slide 65: Group Assignment 2
Use Thevenin’s theorem to find the current in the 5Ω resistor of the circuit below.

## Slide 66: Norton’s Theorem
Theorem:
Any linear circuit connected between two terminals can be replaced by a Norton’s current(IN) in parallel with a Norton's resistance (RN).
RN is the resistance seen from the two terminals when all sources have been deactivated (RN = RTH)
IN is the short-circuit current between the two terminals

## Slide 67: Norton’s Theorem
To find the current through a resistor in a circuit, the following steps are taken:
Remove the resistor from the circuit and mark the two terminals.

## Slide 68: Norton’s Theorem
2. Find the short-circuit current (IN) through the two terminals by applying KVL.

## Slide 69: Norton’s Theorem
3. Recall the circuit created before step 2 and deactivate all sources. Short-circuit voltage sources and Open-circuit current sources.

## Slide 70: Norton’s Theorem
4. Find the total resistance of the circuit resulting from step 3 as
seen from the two terminals

## Slide 71: Norton’s Theorem
5. Reproduce the Norton’s equivalent circuit and connect the resistor whose current is to be found.

## Slide 72: Norton’s Theorem
6. Calculate the current in the circuit in step 5. This is the current being sought for.
I

## Slide 73: Norton’s Theorem
Example 1
Using Norton’s theorem, determine the current in the 3-Ω resistor of the circuit below.
Steps 1 & 2
Solution

## Slide 74: Norton’s Theorem
Applying KVL to loop abefa:
Applying KVL to loop cbedc:

## Slide 75: Norton’s Theorem
Substituting for I in equation 1:
Steps 3 & 4

## Slide 76: Norton’s Theorem
Steps 5 & 6

## Slide 77: Norton’s Theorem
Example 2
Determine the current in the load resistor RL
Solution

## Slide 78: Norton’s Theorem
Solution
Applying KCL

## Slide 79: Norton’s Theorem
Finding RN

## Slide 80: Norton’s Theorem
Finding IL

## Slide 81: Superposition Theorem
The Theorem
The current through(or the voltage across) any element in a multiple-source linear circuit can be found by taking the algebraic sum of the current through(or the voltage across) that element due to each individual source acting alone

## Slide 82: Superposition Theorem
The Theorem
+

## Slide 83: Superposition Theorem
With the 35V battery acting alone,

## Slide 84: Superposition Theorem
With both batteries acting,
+
=

## Slide 85: Reciprocity Theorem
The Theorem
An ideal ammeter and ideal voltage source when inserted in two different branches of a linear network can be interchanged without changing the reading of the ammeter
=

## Slide 86: Reciprocity Theorem
Example 1
Jointly use superposition and reciprocity theorems to find the current supplied by the 35V battery of the circuit below.
Solution
With the 42V battery acting alone,

## Slide 87: Reciprocity Theorem

## Slide 88: Reciprocity Theorem
The second circuit to be solved is:
is comparable to
Applying the reciprocity theorem
=

## Slide 89: Reciprocity Theorem

## Slide 90: Reciprocity Theorem
Use Norton’s theorem to find the current in the 2Ω resistor connected between e and f in the circuit below.
Submission date: God willing a week today
Submission time: Before lecture starts
Where to submit: Class room

## Slide 91: Delta-star Transformation
The transformation is employed in situations where neither series nor parallel arrangements can be identified.
An arrangement of three(3) resistors where one terminal of a resistor is connected to another resistor and the other terminal to a different resistor is a delta arrangement.

## Slide 92: Delta-star Transformation
An arrangement of three(3) resistors where all resistors have a common point of connection through one terminal of each resistor while the remaining terminals are unconnected or connected to elements other than the two other resistors is a star(wye) arrangement.

## Slide 93: Delta-star Transformation
A delta arrangement can be changed to star and vice versa using the following relations:

## Slide 94: Star-Delta Transformation
When all values are the same, delta values are 3 times star values

## Slide 95: Delta-star Transformation
Example 1
Determine the voltage V0 across the 6Ω resistor of the circuit below
Solution

## Slide 96: Delta-star Transformation
Example 1
Determine the voltage V0 across the 6Ω resistor of the circuit below

## Slide 97: Group Assignment 4
Use Norton’s theorem to find the current in the 3Ω resistor connected between points A and B of the circuit below.
Submission date: God willing a week today
Submission time: Before lecture starts
Where to submit: Electrical Engineering office