## Slide 1
EE 151
APPLIED ELECTRICITY
2016.09.06
Ing. Dr. Abdul-Rahman Ahmed

## Slide 2: Alternating Current Circuits
Alternating current (AC) circuits are circuits with currents and voltages which are time-varying
Examples of AC waveforms are:
Sine wave
Square wave
Triangular wave

## Slide 3: Terminologies In Ac Circuits
Amplitude (peak): The maximum deviation of the function from its center position
Cycle: A repeating portion of a function (wave).
Period (T): The duration of a cycle,
Frequency( f ): The inverse of period.
A B C

## Slide 4: Average Value
Average value: The average value of a periodic function is its dc value.
If
Then

## Slide 5: Average Value
The following steps are followed when finding average values of waveforms:
Identify a cycle of the wave
Note the period
Find the area of the cycle
Divide the area by the period
Identify a cycle of the wave
2. Note the period
3. Find the area of the cycle
4. Divide the area by the period

## Slide 6: Root Mean Square Value
The Root Mean Square (RMS) or Effective value of an alternating quantity is the value of a direct current which when flowing through a given resistance for a given time produces the same heat as produced by the alternating current when flowing through the same resistance.
The RMS value of an alternating current
is

## Slide 7: Root Mean Square Value
The following steps are taken when finding the RMS value of a waveform
Identify a cycle of the waveform
Note the period
Square the cycle
Find the area under the squared cycle
Divide the area by the period
Take the square root of the result
Identify a cycle of the waveform
Note the period
Square the cycle
Find the area under the squared cycle
Divide the area by the period
Take the square root of the result

## Slide 8: Root Mean Square and Average Value
Example 1
Find the average and rms values of the waveform below.
Average Value
Cycle spans from 0 to 4
Period= 4s
Area of cycle

## Slide 9: Root Mean Square and Average Value

## Slide 10: Root Mean Square Value
RMS value
Cycle spans 0 to 4
Period = 4s
Squared cycle
Area covered by squared cycle
Division of area by period

## Slide 11: Root Mean Square Value
Taking square root

## Slide 12: Root Mean Square Value
Example 2
Calculate the effective value of the voltage below.
Solution
Cycle spans from 0 to 2π
Area of sine part

## Slide 13: Root Mean Square Value
Area of triangular part
Total area:
Mean

## Slide 14: Root Mean Square Value
RMS value

## Slide 15: Sinusoidal Voltages And Current
Voltages and currents of commercial ac generators have the following expressions:
or
is the peak voltage
is the frequency in Hz
Is the angular frequency in radian per second.
It specifies how many oscillations occur in a unit time interval

## Slide 16: Sinusoidal Voltages And Current
or
is the peak current
is the frequency in Hz
Is the angular frequency in radian per second. It specifies how many oscillations occur in a unit time interval

## Slide 17: Rms Value Of Sinusoidal Quantities
The RMS value of a sinusoidal voltage
is given by:

## Slide 18: Rms Value Of Sinusoidal Quantities
Similarly,
The RMS value of a sinusoidal current
is given by:

## Slide 19: Rms Value Of Sinusoidal Quantities
Example 1
Find the rms values of the following quantities:
(a)
(b)
Solution
(a)
(b)

## Slide 20: Harmonics
Non-sinusoidal periodic voltages and currents can be expressed as the sum of sine waves in which the lowest frequency is f and all other frequencies are integral multiples of f.
For example, a square wave of amplitude E can be expressed as:

## Slide 21: Harmonics
Any quantity which contains multiple frequencies is a harmonic quantity.
The frequency of which others have been expressed as multiples of is the fundamental frequency.
An odd multiple of the fundamental is an odd harmonic.
An even multiple of the fundamental is an even harmonic.

## Slide 22: Rms Value Of A Harmonic Quantity
The effective value of a harmonic quantity is obtained by:
First obtaining the square of the rms value of each term
Adding the obtained squared rms values
Taking the square root of the sum

## Slide 23: Rms Value Of A Harmonic Quantity
Example
Find the RMS value of the current
Solution

## Slide 24: Phasors
Phasors are used to represent sinusoidal quantities to avoid drawing the sine waves.
A phasor is a straight line whose length is proportional to the rms voltage or current it represents.
To show the phase angle or phase displacement between voltages and currents, the phasors bear an arrow.

## Slide 25: Phasors
Two phasors are said to be in phase when they point in the same direction. The phase angle between them is then zero.

## Slide 26: Phasors
Two phasors are said to be out of phase when they point in different directions.
The phase angle between them is the angle through which one of them has to be rotated to make it point in the same direction as the other.

## Slide 27: Phasor Diagrams
It is used to show at a glance the magnitude and phase relations among the various quantities within a network. This is often helpful in the analysis of the network.
Example
A 50 Hz source having rms voltage of 240 V delivers a rms current of 10 A to a circuit. The current lags the voltage by 30°.
Draw the phasor diagram for the circuit.
(b) Express the voltage and current as functions of time.

## Slide 28: Phasor Diagrams
Solution
(a) Taking V as the reference
(b)

## Slide 29: Addition And Subtraction Of Sinusoidal Quantities
The sum of sinusoidal quantities is obtained by taking the vector sum of their phasors.
The difference of sinusoidal quantities is obtained by first reversing the subtracted quantity and adding it as a vector to the other phasors.
A sinusoidal quantity is reversed by adding 1800 to its angle
Only sinusoidal quantities of the SAME FREQUENCY can be added or subtracted.

## Slide 30: Addition And Subtraction Of Sinusoidal Quantities
Example 1
Let v1(t) = 60 sin ωt and v2(t) = 80 sin (ωt – 90°). Determine (a) v1 + v2 and (b) v1 – v2
Solution
(a) Phasor diagram

## Slide 31: Addition And Subtraction Of Sinusoidal Quantities
(b)
Phasor diagram

## Slide 32: Addition And Subtraction Of Sinusoidal Quantities

## Slide 33: Addition And Subtraction Of Sinusoidal Quantities
Example 2
Four conductors meet at a junction. The following relationship exists between them.
Find the value of given that

## Slide 34: Addition And Subtraction Of Sinusoidal Quantities
Solution
(a) There are two different frequencies. They must therefore be
added separately.
Addition of part.
X-component
Y-component

## Slide 35: Addition And Subtraction Of Sinusoidal Quantities
Amplitude
Angle
Therefore, part of is

## Slide 36: Addition And Subtraction Of Sinusoidal Quantities
Addition of part.
X-component
Y-component
Amplitude

## Slide 37: Addition And Subtraction Of Sinusoidal Quantities
Angle
Therefore, part of is
Hence

## Slide 38: Group Assignment 5
Four circuit elements are connected in series across a sinusoidal alternating voltage given by . The instantaneous voltage across three of the elements are given by
(a)Determine the expression for the fourth voltage in the form
(b) What is the r.m.s. value of v4?
Use phasor diagrams. DO NOT use complex number approach

## Slide 39: Impedance (Z)
The opposition to current flow in ac circuits owing to the presence of combinations of resistive, inductive and capacitive elements.
Opposition due to inductance (L) is called inductive reactance(XL).
Opposition due to capacitance is called capacitive reactance(XC).

## Slide 40: Impedance (Z)
Phase relationship between the current and voltage in a resistor
Let
It is noted that the voltage across and the current through a resistor are
in phase.

## Slide 41: Impedance (Z)
Phase relationship between the current and voltage in an inductor
Let
It is noted that the current through an inductor lags the voltage by 900.

## Slide 42: Impedance (Z)
Phase relationship between the current and voltage in an inductor
Let
It is noted that the current through an inductor lags the voltage by 900.

## Slide 43: Impedance (Z)
Phase relationship between the current and voltage in a capacitor
Let
It is noted that the current through a capacitor leads the voltage by 900.

## Slide 44: Impedance (Z)
Series circuit containing R and L

## Slide 45: Impedance (Z)
Phase angle between current and voltage in a series RL circuit
The current in a series RL circuit lags the voltage but not by 900

## Slide 46: Impedance (Z)
Series circuit containing R and C

## Slide 47: Impedance (Z)
Phase angle between current and voltage in a series RL circuit
The current in a series RC circuit leads the voltage but not by 900

## Slide 48: Impedance (Z)
Series circuit containing R, L and C

## Slide 49: Impedance (Z)

## Slide 50: Impedance (Z)
Phase angle between current and voltage in a series RLC circuit
Current in a series
RLC circuit may lead or lag the voltage depending on the relative values of XL and XC

## Slide 51: Impedance (Z)
Example 1
A coil has R=12Ω and L=0.1H. It is connected across a 100V, 50Hz supply. Calculate (a) the reactance and impedance of the coil (b) the current and (c) the phase difference or angle between the current and the applied voltage.

## Slide 52: Impedance (Z)
Solution
(a)
(b)

## Slide 53: Impedance (Z)
(c)

## Slide 54: Impedance (Z)
Example 2
A metal filament lamp, rated at 750W, 100V is to be connected in series with a capacitor across a 230V, 50Hz supply. Calculate (a) the capacitance required and (b) the phase angle between the current and supply voltage.
Solution
(a)

## Slide 55: Impedance (Z)
(a)
Hence,

## Slide 56: Impedance (Z)
(b)

## Slide 57: Power In Ac Circuits
There are three kinds of power in ac circuits
Apparent Power (S) which is measured in Volt-amperes (VA)
Active Power (P) which is measured in Watts (W).
Active Power is also called Actual Power, Useful Power, True Power, Real Power or simply, Power
3. Reactive Power (Q) which is measured in Volt-amperes reactive (VAR)

## Slide 58: Power In Ac Circuits
There following relationships exist between S, P and Q
is called power factor (pf)

## Slide 59: Power In Ac Circuits
Power factor may be said to be lagging or leading.
Power factor is lagging when current lags voltage
Power factor is leading when current leads voltage

## Slide 60: Power In Ac Circuits
Relationships between the three passive elements , P and Q
Resistors consume only P
Inductors consume only Q
Capacitors do not consume P and Q. They rather supply Q or reduce the consumption of Q.

## Slide 61: Power In Ac Circuits
Example 1
A single-phase motor connected to a 400-V, 50-Hz supply is developing 10 kW with efficiency of 84 per cent and a power factor of 0.7 lagging. Calculate (a) the input kVA (b) the active and reactive components of the current and (c) the reactive kVA.
Solution
(a)

## Slide 62: Power In Ac Circuits
(b)

## Slide 63: Power In Ac Circuits
(b)

## Slide 64: Power In Ac Circuits
Example 2
An emf whose instantaneous value is given by 283sin(314t + π/4)V is applied to an inductive circuit and the current in the circuit is 5.66sin(314t – π/6)A. Determine (a) the frequency of the emf (b) the R and L (c) the power absorbed.
Solution
(a)
(b)

## Slide 65: Power In Ac Circuits
(b)

## Slide 66: Power In Ac Circuits
(c)

## Slide 67: Using Complex Numbers To Solve Ac Circuit Problems
The ability to make a vector quantity appear as a scalar quantity using complex numbers is utilized in the analysis of ac circuits.
All the mathematical manipulations in complex algebra hold when employing complex numbers in analyzing ac circuits.
The operator ‘i’ is replaced with ‘j’ in other to avoid confusing it with current.

## Slide 68: Using Complex Numbers To Solve Ac Circuit Problems
The three passive elements are represented as follows:
as a complex number is
as a complex number is
as a complex number is

## Slide 69: Using Complex Numbers To Solve Ac Circuit Problems
Example 1
Express in rectangular and polar notations, the impedance of each of the following circuits at a frequency of 50 Hz: (a) a resistance of 20 Ω (b) a resistance of 20 Ω in series with an inductance of 0.1 H (c) a resistance of 50 Ω in series with a capacitance of 40 μF.
Solution
(a)
(b)

## Slide 70: Using Complex Numbers To Solve Ac Circuit Problems
(c)

## Slide 71: Using Complex Numbers To Solve Ac Circuit Problems
Example 2
A circuit is arranged as indicated in the figure below, the values being as shown. Calculate the value of the current in each branch and its phase relative to the supply voltage.
Solution

## Slide 72: Using Complex Numbers To Solve Ac Circuit Problems
Choosing the voltage a the reference phasor,

## Slide 73: Using Complex Numbers To Solve Ac Circuit Problems
Current leads supply voltage by 44.20
Current leads supply
voltage by 73.680

## Slide 74: Using Complex Numbers To Solve Ac Circuit Problems
Current lags supply voltage by 7.270

## Slide 75: Using Complex Numbers To Solve Ac Circuit Problems
Q is positive when the current lags the voltage
Q is negative when the current leads the voltage

## Slide 76: Calculation Of Complex Power
Example 1
The potential difference across and the current in a circuit are represented by 100 + j200 v and 10 + j5 a respectively. Calculate the power and reactive voltamperes (or vars).
Solution

## Slide 77: Calculation Of Complex Power
Example 2
A small installation consists of the following loads connected in parallel across a single-phase 240V, 50Hz supply:
(a) a fan motor taking an input of 1.5kVA at 0.75pf lag,
(b) a 1000W radiator operating at unity power factor
(c) a number of fluorescent lamps taking a total load of 1.2kVA at 0.95pf lagging
Find the total current, kW, kVA and power factor of the load.

## Slide 78: Calculation Of Complex Power
Solution
The problem is solved by obtaining the active and reactive component of each load and then summing all reactive components and all active components
Load (kVA) | cosϕ | P(kW) = Scosϕ | sinϕ | Q(kVAR) = Ssinϕ
TOTAL |  |  |  | 

## Slide 79: Calculation Of Complex Power

## Slide 80: Calculation Of Complex Power
NOTE
In the problem above, if one load had a leading power factor, then its Q would have a negative sign and thus would have subtracted from the others.

## Slide 81: Group Assignment 6
A small installation consists of the following loads connected in parallel across a single-phase 240V, 50Hz supply:
(a) a fan motor having an input of 2kVA at 0.75pf lag,
(b) a 1.5kW radiator operating at unity power factor,
(c) a 1kVA load operating 0.85 leading power factor.
Find the total current, kW, kVA and power factor of the load.