## Slide 1
EE 151
APPLIED ELECTRICITY
2016.09.06
Ing. Dr. Abdul-Rahman Ahmed

## Slide 2: Three-Phase Circuits
A single-phase generator produces a single sinusoidal voltage.
A 3-phase generator on the other hand produces three equal voltages which are out of phase with one another by 120o.
The three voltages are generated in three separate windings arranged in a special way in the machine.
A 3-phase system is a power supply system consisting of three voltages which are 120o out of phase with one another.
Three-phase systems have the following advantages over single phase systems
Three-phase motors, generators and transformers are simpler, cheaper and more efficient
Three-phase transmission lines can deliver more power for a given weight and cost
The voltage regulation of three-phase transmission lines is inherently better
A 1-phase supply can be obtained from a 3-phase one

## Slide 3: 3-Phase Winding

## Slide 4: Examples: 33 kV Transmission (GRIDCO)

## Slide 5: Examples: 11 kV Distribution (ECG)

## Slide 6: Examples: 415 V to Customers (ECG)

## Slide 7: Three-phase Circuits
The two main connections of three-phase windings
A star arrangement where all winding have a common point
Letters a, b and c , colours red (R), yellow(Y) and blue (B) or numbers 1, 2 and 3 are used to name the windings

## Slide 8: Three-phase Circuits
2. A delta arrangement where all winding are connected to each other
Letters a, b and c , colours red (R), yellow(Y) and blue (B) or numbers 1, 2 and 3 are used to name the windings

## Slide 9: Three-phase Circuits
The phasor diagram for the three-voltages (in star or delta) is indicated below.

## Slide 10: Three-phase Circuits
Line and phase voltages
The voltage from one line to another is call a line-to-line voltage or simple a line voltage
The voltage across each winding is a phase voltage
On a phasor diagram, a line voltage is drawn from the end of one phase to another in the anti clockwise direction

## Slide 11: Three-phase Circuits
Relationship between Line and phase voltages for a star connection

## Slide 12: Three-phase Circuits
Hence, for a star connection, the line voltage is times the phase voltage

## Slide 13: Three-phase Circuits
Relationship between Line and phase voltages for a delta connection

## Slide 14: Three-phase Circuits
Relationship between Line and phase current for a star connection

## Slide 15: Three-phase Circuits
Relationship between Line and phase currents for a delta connection

## Slide 16: Three-phase Circuits
Hence, for a delta connection, the line current is times the phase current

## Slide 17: Three-phase Circuits
Analysis of three-phase balanced circuits
A balanced three-phase circuit is that in which identical loads are connected in each phase.
The currents that flow in a balanced three-phase system are equal in magnitude and also 120° out of phase.
A balanced three-phase circuit is analysed by considering just one phase
When finding total power, the per phase power is multiplied by three
1-phase power factor is the same as in 3-phase

## Slide 18: Three-phase Circuits
Example 1
Three identical resistors are connected in star across a 3-phase, 415-V supply. If each resistor has a resistance of 50 ohms, calculate (a) the voltage across each resistor (b) the current in each resistor (c) the total power supplied to the load
Solution
(a)
(b)

## Slide 19: Three-phase Circuits
(c)

## Slide 20: Three-phase Circuits
Example 2
Three identical impedances are connected in delta across a 3-phase, 415-V supply. If the line current is 10 A, calculate (a) the current in each impedance (b) the value of each impedance.
Solution
(a)
(b)

## Slide 21: Three-phase Circuits
Example 3
A 3-phase, 450-V system supplies a balanced delta-connected load of 12 kW at 0.8 power factor lagging. Calculate (a) the phase currents (b) the line currents and (c) the effective impedance per phase.
Solution
(a)

## Slide 22: Three-phase Circuits
(b)
(c)

## Slide 23: Three-phase Circuits
Power in three-phase circuits
The total apparent power of a balanced three-phase circuit (star or delta) is given by:
The total active power of a balanced three-phase circuit (star or delta) is given by:
The total reactive power of a balanced three-phase circuit (star or delta) is given by:

## Slide 24: Three-phase Circuits
Analysis of parallel balanced three-phase circuit problems
When the parallel loads are not of the same kind(say one is delta and the other is star), then they must be changed either all to star or all to delta.
When all are in star, the circuit is analyzed by taking one phase of each and applying the star characteristics.
When all are in delta, the circuit is analyzed by taking one phase of each and applying the delta characteristics.

## Slide 25: Three-phase Circuits
Parallel circuit are better analysed by reverting to complex numbers.
Example 1
A Y-connected impedance Z1 = 20.0 + j37.75 Ω per phase is connected in parallel with ∆-connected impedance Z2 = 30.0 – j159.3 Ω per phase. For an impressed 3-phase voltage of 398 V line to line, compute the line current, power factor and the power taken by the parallel combination.
Solution
The circuit is solved by making all star.

## Slide 26: Three-phase Circuits
Y-connected impedance Z1 = 20.0 + j37.75 Ω
∆-connected impedance Z2 = 30.0 – j159.3 Ω
Changing the delta to star

## Slide 27: Three-phase Circuits

## Slide 28: Three-phase Circuits
Example 2
A manufacturing plant draws 415 kVA from a 2400 V, 3-phase line. If the plant power factor is 0.875 lagging, calculate (a) the impedance of the plant per phase (b) the phase angle between the phase voltage and phase current.
Solution
The load is considered to be star.
(a)

## Slide 29: Three-phase Circuits

## Slide 30: Three-phase Circuits
Example 3
A star-connected motor is connected to a 4000 V, 3-phase, 50 Hz line. The motor produces an output power of 2681 kW at efficiency of 93 % and a power factor of 0.9 lagging. Calculate (a) the active power absorbed by the motor, (b) the reactive power absorbed by the motor, (c) the apparent power supplied by the transmission line and (d) the motor line current.
Solution
(a)

## Slide 31: Three-phase Circuits
(a)
(b)
    (c)

## Slide 32: Three-phase Circuits
(d)

## Slide 33: Three-phase Circuits
(a)Three-phase four-wire feeding unbalanced star-connected loads
Three-phase unbalanced load does not have the same impedance in all the three phases.
The neutral points of the source and the load are the same, so the voltage across each phase of the load is the phase voltage of the source
Three-phase four wire is usually used for low-voltage power distribution
The neutral carries current if the load is unbalanced

## Slide 34: Three-phase Circuits
Each phase is analyzed separately when the load is unbalanced
Example 1
A three-phase four-wire system has the following data: Supply voltage is 415 V, Z1 = 8 + j0 Ω, Z2 = 0 - j8 Ω and Z3 = 0 + j8 Ω. Determine the load currents and the current in the neutral.
Solution

## Slide 35: Three-phase Circuits

## Slide 36: Three-phase Circuits

## Slide 37: Three-phase Circuits
Example 2
In a three-phase four-wire system, the line voltage is 400V and resistive loads of 10 kW, 8 kW and 5 kW are connected between the three lines and neutral. Calculate (a) the current in each line and (b) the current in the neutral conductor.
Solution
(a)

## Slide 38: Three-phase Circuits
Let Ia, Ib and Ic be the currents drawn by the 10kW, 8kW and 5kW loads respectively.

## Slide 39: Three-phase Circuits