## Slide 1
EE 151
APPLIED ELECTRICITY
2016.09.06
Ing. Dr. Abdul-Rahman Ahmed

## Slide 2: Magnetic Circuits
A magnetic circuit is a closed path followed by any group of lines of magnetic flux.
Magnetic circuits are created with coils and ferromagnetic (iron, cobalt, nickel, etc) or permanent magnetic materials.

## Slide 3: Magnetic Circuits
Terminologies in magnetic circuits
Flux(ϕ)
It is a measure of the amount of magnetic field passing through a given surface. The SI unit of flux is Weber(Wb).
Flux density (B)
It is the flux per unit area. It is the flux divided by the cross-sectional area. The SI unit is Weber per square meter (Wb/m2) or Tesla (T)

## Slide 4: Magnetic Circuits
Terminologies in magnetic circuits
Magnetomotive force (F)
It is the source which sets up the flux flowing around a magnetic circuit. The unit is Amperes (A) or Ampere-turns(AT). It is the product of current in coil and number of turns of coil

## Slide 5: Magnetic Circuits
Reluctance(S or )
It is likened to resistance. It is the opposition offered by a material to the flow of magnetic flux.
is the length of the magnetic path in meters (m)
is the cross sectional area in square meter (m2)
The unit of reluctance is ampere-turns per weber (AT/Wb)

## Slide 6: Magnetic Circuits
Terminologies in magnetic circuits
Magnetic field intensity (H)
It is the mmf per unit length. The unit is Amperes per meter (A/m)or Amper-Turns per meter (AT/m)

## Slide 7: Magnetic Circuits
B-H curves
They are curves which show the relation between magnetic flux density and magnetic field intensity for various materials
The B-H curve of vacuum is as shown
    is a constant called magnetic constant or permeability of free space

## Slide 8: Magnetic Circuits
B-H curve of non-magnetic materials
The B-H curves are almost identical to that of vacuum.

## Slide 9: Magnetic Circuits
B-H curve of magnetic materials
The B-H curves have linear, non-linear and saturation regions
    is a the relative permeability of the magnetic material.
    The above formula only works for the linear region.

## Slide 10: Magnetic Circuits
Analysis of linear magnetic circuits
Magnetic circuits are analyzed by drawing an equivalent electric circuit and applying the laws used to analyze electric circuits. The following similarities exit.
Flux is similar to current
Magnetomotive force is similar to electromotive force
Reluctance is similar to resistance

## Slide 11: Magnetic Circuits
Analysis of non-linear magnetic circuits
Not all the laws of electric circuits can be applied to magnetic circuits. Kirchoff’s laws are applicable and when applied to magnetic circuits are stated as follows:
First law: The total magnetic flux towards a junction is equal to the total magnetic flux away from that junction.
Second law: In any closed magnetic circuit, the algebraic sum of the product of magnetic field strength and the length of each part of the circuit is equal to the resultant magnetomotive force.

## Slide 12: Magnetic Circuits
Example 1
A 600-turn coil carrying a current of 0.2A sets up a flux of 200mWb in a magnetic circuit.
(i) What is the mmf in amperes developed in the circuit?
(ii) Determine the total reluctance of the circuit.

## Slide 13: Magnetic Circuit
Example 2
The figure below shows the equivalent electric circuit of a three-part magnetic circuit energised by a 100-turn coil carrying a current of 1A. The mmf drop across part ‘b’ is 40AT

## Slide 14: Magnetic Circuit
Calculate the flux in part c.
Determine the reluctance of parts b and c.
Obtain the flux density in part b if the cross sectional area of the material used is 0.05m2.

## Slide 15: Magnetic Circuit
Example 3
A magnetic circuit comprises three parts in series each of uniform cross section. They are (a) a length of 80 mm and cross sectional area 50mm2 (b) a length of 60mm and cross sectional area 90 mm2 (c) an air gap of length 0.5 mm and cross sectional area 150mm2 . A coil of 4000 turns is wound on part (b) and the flux density in the air gap is 0.3 T. Assuming that all the flux passes through the given circuit and that the relative permeability of section (a) and (b) is μr = 3000, estimate the coil current to produce such a flux density.

## Slide 16
Solution
The electric analogue circuit is shown below.

## Slide 17: Magnetic Circuit

## Slide 18: Magnetic Circuit
Example 4
A steel ring of cross-sectional area 50mm2 has an air gap of 2mm and of the same cross-sectional area as shown in Fig. below. The coil shown has 2000 turns with current 10 A. If the mean radius of the steel ring is 5cm and μr = 800, calculate (a) the total reluctance of the circuit (b) the flux Φ in the ring.
    Solution
    (a) The equivalent electric circuit is as shown

## Slide 19: Magnetic Circuit

## Slide 20: Magnetic Circuit
    Total reluctance
    (b)

## Slide 21: Magnetic Circuit
Example 5
    It is desired to produce a magnetic field of 1 Wb/m2 in the air gap of the electromagnet shown in Example 2. The cross section of the iron is 1 cm2, the mean length Li + Lg = 10 cm, gap length Lg = 5 mm, and from the B-H curve of the iron μr was found to be 500 at B = 1 Wb/m2. Calculate the m.m.f. required.
    Solution

## Slide 22: Magnetic Circuit

## Slide 23: Magnetic Circuit
Example 6
A coil of 1500 turns is wound on a circular wooden former which has a mean circu-mference of 30cm and a cross-sectional area of 4cm2. Calculate (a) the flux density in the ring when the coil carries a current of 0.4 A (b) the flux in the ring in webers.
When the wooden former was replaced with a steel former of the same dimension, the total flux became 600μWb for a current of 0.4 A. Calculate the relative permeability of the steel and the reluctance of the magnetic circuit at this flux density.

## Slide 24: Magnetic Circuit
Solution
A coil of 1500 turns is wound on a circular wooden
(a)

## Slide 25: Magnetic Circuit
With the magnetic former